Cover Sheet

| Source of Leveraged Topographic Data: | University of New Hampshire |
| --- | --- |
| County / State: | Rockingham County, New Hampshire |
| MIP Case Number: | 12-01-1574S |
| Data Submitted through MIP Workflow Task? | Yes No (default) |
| Extents of Topographic Data Received: | West Bounding Coordinate: -71.522532, East Bounding Coordinate: -70.500274, North Bounding Coordinate: 43.649523, South Bounding Coordinate: 42.686320 |
| Extents of Topographic Data Reviewed: | Same as above |
| List of Files Being Reviewed: (attach a file listing if there are too many to list here): | Terrain Bare Earth DEM dem_10ft.rar Contours Merged_Bathymetry_PTS_3d.shp TIN R0000 – R0348 H11014_MLLW.xyz |
| Has a data sharing agreement been provided? (for non-public data provided solely for the purpose of the study) | Yes No (Attach data sharing agreement if available) |
| PTS Proj. Manager (Name & Date) | Jeffrey Burm, PE, CFM, AECOM, January, 2012 |
| PTS QC Reviewer (Name & Date) | Fay Rubin, University of New Hampshire, July, 2012 |
| Other Reviewer (Name & Date) |  |

Information Specific to All Received Topographic Datasets

| Item # | Question, Direction, or Requirement: | Definition or Details: | Review Assessment: Pass, Fail, or Partial Fail | Comments: |
| --- | --- | --- | --- | --- |
| 1 | Project Date | Source Data Acquisition Date: (Month/Year) May, 2011 Start Date: 05/06/2011 Last flight Date: 05/30/2011 |  |  |
| 2 | Type of digital topographic data received: | Data Model type: (choose one or more): Contours (Interval _____________) Derivation: Photogrammetric LiDAR/TIN/DEM Cross sections Mass points (LiDAR, etc.) Breaklines TINs DEMs |  |  |
| 3 | Surface Type: | Surface Description (choose one): Bare Earth (FEMA default) Top Surface (tree tops/roof tops) (Fail) Bathymetric surface | Pass |  |
| 4 | Vertical Accuracy - What is the Vertical Accuracy of the delivered data? | Vertical Accuracy (choose one) 1’ contour equiv. (Accuracy = 0.6 ft.) 2’ contour equiv. (Accuracy = 1.2 ft.)* 4’ contour equiv. (Accuracy = 2.4 ft.) 5’ contour equiv. (Accuracy = 3.0 ft.) Other Accuracy – See Comments * Vertical accuracy at the 95% confidence level (Accuracyz) = RMSEz x 1.9600 with normal distribution as stated in the metadata | Pass |  |
| 5 | Horizontal Accuracy – What is the Horizontal Accuracy of the delivered data? | Horizontal Accuracy as Compiled (choose one): 1” = 500’ equiv. (NSSDA RMSEr = 11’ or 3.35 m) 1” = 1000’ equiv. (NSSDA RMSEr= 22’ or 6.67 m) 1” = 2000’ equiv. (NSSDA RMSEr= 26.3’ or 8.02 m) Bathymetric surface RMSE = 1 m Other Accuracy – See Comments Horizontal accuracy as stated in the metadata, at the 95% confidence level: (NSSDA Accuracyr) = NSSDA RMSEr x 1.7308 | Pass | LiDAR was collected on average of 2.0 meter point spacing or better |
| 6 | Reporting - | Was a report provided detailing the methodologies used in preparing these datasets? Yes No Was Federal Geographic Data Committee (FGDC) compliant Metadata file provided? Yes No |  |  |
| 7 | Ellipsoid and Geoid models used to obtain orthometric heights used in this dataset: | Ellipsoid Model: Clarke (1878) WGS-72 GRS-80 WGS-84 NAD27 Ellipsoid NAD83 Ellipsoid Unknown Geoid Model: (if provided in metadata) Geoid09 Geoid06 Geoid03 Geoid99 Older Geoids Other ____________ |  |  |
| 8 | Does the Topographic metadata list any LiDAR / TIN /DEM areas that may not meet the stated vertical accuracy? | Are there any areas reported by the provider that may not meet the stated vertical accuracy? Yes No Specific types of non-compliant areas mentioned (choose one or more): Open Water Steep Terrain Dense Forest New Asphalt Are the locations of these non-compliant areas documented? Yes No |  | Narrative provided by contractor describes use of NED 1/3 Arc Second DEM data to capture study streams’ contributing drainage area, and NOS bathymetric data for off-shore areas. |

Information Specific to Reviewed Topographic Datasets

| Item # | Question, Direction, or Requirement: | Definition or Details: | Review Assessment: Pass, Fail, or NR (Not Required) | Comments: |
| --- | --- | --- | --- | --- |
| 9 | Type of digital topographic data reviewed: | Data Model type: (choose one or more): Contours (Interval _____________) Derivation: Photogrammetric LiDAR/TIN/DEM Cross sections Mass points (LiDAR, etc.) Breaklines TINs DEMs |  |  |
| 10 | Data attributes of reviewed materials: | Coordinate System: (choose one) UTM State Plane Geographic Other:________________________________ Unknown (requires “Fail”) Coordinate System Units: (choose one) Feet (U.S.) Feet (International) Meters Other:_____________ Decimal Degrees to _____ Decimal Places Unknown (requires “Fail”) Horizontal Datum: (choose one) NAD 27 NAD 83 (default) Unknown (requires “Fail”) Vertical Datum: (choose one) NGVD 29 NAVD 88 Other (MLLW, etc.)_______________________ Unknown (requires “Fail”) Vertical Units: Feet to __2__ Decimal Places Meters to ____ Decimal Places Other:_____________ to ____ Decimal Places Unknown (requires “Fail”) Coverage: (choose one): Continuous Tiled Irregular | Pass |  |
| 11 | Data Formats of reviewed material: | DEM Data Formats: ASCII xyz BIL BIP BSQ DEM USGS ESRI Grid (Floating Point) ESRI Grid (Integer) GeoTiff RLE Other: __________________ Contour Lines and Breakline Formats: DGN v._______ DWG v. _______ DXF v. ________ DLG-O (DLG-Optional) .E00 MIF/MID SHP ESRI pGDB SDTS TAB Other: __________________ LiDAR, Mass Points, and TIN Formats: LAS v. _______ ASCII xyz ASCII with attribute data BIN ESRI TIN ESRI TIN Arc/Info Export ESRI Arc9.3 Terrain Other: ______________________________________ |  |  |
| 12 | Data Coverage of reviewed material– Does the data cover the area to be studied, including the 0.2% chance flood hazard and sufficient buffer area? | Data Coverage Over Entire Study Area: Yes No (see comments) |  |  |
| 13 | Post-Processed? | Does the data appear to be bare-earthed? Yes No (Fail/Partial Fail) | Pass |  |
| 14 | Post – Processing Issues: | Are there any issues with the post-processing to bare earth (structures or trees not removed, etc.)? Yes (Fail/Partial Fail) No | Pass |  |
| 15 | Ground Control - Network Control Points | Were National Geodetic Survey (NGS) data sheets for Network Control Points found and used in the QC? Yes No Unknown If Yes, how many? ______________ |  | Source LiDAR data was fully QA/QC’ed by USGS, with associated documentation provided. |
| 16 | Optional Enhancements Hydro-Enforcement and Bridges/Culverts | Is the data hydro-enforced? Yes No Are bridges / culverts removed? Yes No |  |  |
| 17 | Data Voids – Are there data voids in the area of potential floodplain? | Data Voids In the Floodplain? Yes No Are the locations of these data void areas documented? Yes No Is additional ground survey or interpolation needed to fill voids in the potential floodplain areas? Yes No | Pass | Describe data void issues, grab screenshots, and provide comments: |
| 18 | Artifacts – Have artifacts been noticed in the area of potential floodplain in the extent of the data being reviewed? | Have artifacts been noticed? Yes artifacts exist & may affect mapping No | Pass | Describe artifact issues, grab screenshots, and provide comments: |
| 19 | TIN Specifics | Average LiDAR / TIN post spacing? _______________ |  | If applicable |
| 20 | DEM Specifics | DEM cell size (post spacing)? 50-ft. DEM Derived from LiDAR or TIN? Yes No Other __________________________ |  | Represents resolution of the composite DEM produced in WISE. |

QC Summary

| Issues: | List any issues discovered during this review that need comment. |
| --- | --- |
| QA/QC Summary: | Summarize the findings of this QA/QC. Topographic data appears to be complete, to meet FEMA specifications, and to be properly documented. |