DEVELOPING 2010 IMPERVIOUS SURFACE ESTIMATES

FOR THE PISCATAQUA REGION ESTUARIES PARTNERSHIP TOWNS

A Final Report to

The Piscataqua Region Estuaries Partnership

Submitted by

David Justice and Fay Rubin

Complex Systems Research Center

Institute for the Study of Earth, Oceans and Space

Morse Hall

University of New Hampshire, Durham, NH 03824

October, 2011

Revised December, 2011

This report was funded in part by a grant from the Piscataqua Region Estuaries Partnership as authorized by the U.S. Environmental Protection Agency’s National Estuary Program.

## Table of Contents

List of Tables	1

List of Figures	1

Project Summary	2

Results and Discussion	3

Project Figures	5 – 13

Project Tables	14 – 25

References	26

## List of Tables

Table 1.  Impervious Surface Acreage and Total Acreage by Subwatershed, 1990

Table 2.  Impervious Surface Acreage and Total Acreage by Subwatershed, 2000

Table 3.  Impervious Surface Acreage and Total Acreage by Subwatershed, 2005

Table 4.  Impervious Surface Acreage and Total Acreage by Subwatershed, 2010

Table 5.  Change in Impervious Surface Acreage by Subwatershed, 1990 – 2010

Table 6.  Impervious Surface Acreage by Maine Towns, 1990, 2000, 2005, and 2010

Table 7.  Impervious Surface Acreage by New Hampshire Towns, 1990, 2000, 2005, and 2010

Table 8.  Accuracy Assessment Error Matrix, 2010

## List of Figures

Figure 1.  Project study area

Figure 2.  Regional mapping of impervious surfaces, 1990

Figure 3.  Regional mapping of impervious surfaces, 2000

Figure 4.  Regional mapping of impervious surfaces, 2005

Figure 5. Regional mapping of impervious surfaces, 2010

Figure 6.  Regional mapping of impervious surfaces, 1990, for the York, ME vicinity

Figure 7.  Regional mapping of impervious surfaces, 2000, for the York, ME vicinity

Figure 8.  Regional mapping of impervious surfaces, 2005, for the York, ME vicinity

Figure 9.  Regional mapping of impervious surfaces, 2010, for the York, ME vicinity

## Project Summary

Estimates of impervious surface acreage for 2010 were generated for the 59-town region covered by the Piscataqua Region Estuaries Partnership (PREP). The project extended previous work done in the region for the years 1990, 2000, and 2005 and relied on the same satellite-based data sources and image processing methodologies.  As a result, standardized impervious surface estimates are now available for a 20-year time period in the PREP region.

The current project mapped impervious surfaces (buildings, pavement, etc.) based on a Landsat 5 Thematic Mapper (TM) image acquired on April 24, 2010.  Processing used both traditional and sub-pixel image classification techniques, as described in previous efforts (see Justice and Rubin, 2006 and Justice and Rubin 2003 for a complete processing description). The current study utilized comparable satellite imagery, and applied consistent techniques to map the PREP area for 2010.

It should be noted that since the completion of the 2005 project, the U.S.  Geological Survey (USGS) has modified its image offerings and now only serves TM data resampled using cubic convolution techniques.   (Resampling algorithms are applied as part of the image registration processing, and describe the way output values are assigned to individual image pixels.)   This is an important consideration because our previous sub-pixel classifications were conducted on data sets processed using nearest neighbor resampling (which is the recommended approach).   While the classification process can be completed using data resampled using alternative techniques, the results may not be as reliable. Since the three previous data sets (1990, 2000, and 2005) were developed using images processed using the preferred nearest neighbor method, and because it is unlikely that features would revert from impervious to non-impervious status, we opted to use the 2005 impervious surface raster as the starting point for the current iteration. Accordingly, the 2005 impervious surface data was used to mask the 2010 TM image with any remaining, unmasked pixels classified using the techniques described in the documents referenced above.

A second departure from previous processing streams is that the TM data is now delivered as a georeferenced, terrain-corrected file. This eliminated the requirement for GRANIT to perform these steps locally.

The data set has been archived in the GRANIT GIS clearinghouse, thereby making it available to the coastal resource community as well as the general public.   The data are appropriate for watershed and subwatershed level characterizations.  Users are discouraged from accessing them to support larger scale mapping and applications.

## Results and Discussion

The primary results of this project are 2010 impervious surface estimates for the towns in the Piscataqua Region Estuaries Partnership (Figure 1).   Figures 2 thru 9 show both small-scale and large-scale illustrations of mapped impervious surface features for the study area. These figures (and especially the large-scale images) show evidence of new housing subdivisions and other development in 2000, 2005, and 2010 relative to the 1990 baseline data.

Tables 1 - 4 summarize these results by subwatershed, reporting acreages at 3 levels (low-range, mid-range, and high-range) for each reporting unit. As noted in prior reports, the subpixel classification reports results within percent impervious ranges.   To convert the ranges to discrete acreage estimates, the low, mid and high points of each range were selected.   All further discussion in this document utilizes the estimate derived from the midpoint of the range.

Note:  The version of the subwatershed boundary data used to generate acreage summaries for this report was made available by the NH Department of Environmental Services in the spring of 2011.  Because the subwatershed boundaries have changed since prior reports, all acreages in Tables 1-4 were regenerated based on the new delineations and may differ from those reported in prior impervious surface project reports.

Table 1 reveals that 40,277 acres, or 4.1% of the land surface area in the 73 subwatersheds, were estimated to be impervious in 1990. By the year 2000, Table 2 reports that the acreage had increased to 60,028 acres (6.1%), a marked increase of 19,751 acres.  This represents a 2% increase in impervious surface coverage over the ten-year period (see Table 5). By 2005, the impervious area was estimated at 70,666 acres, an additional 1.1% from that of 2000. In the current time step (2010), impervious surface estimates have increased to 88,870 acres or 9.0% of the land area in the 59-town study area. In comparison to the rate of increase between 2000 and 2005 (1.1%), the 2005 – 2010 percent increase was larger, at 1.8% (see Table 5).

At the subwatershed level, the Portsmouth Harbor unit recorded the highest percentage of impervious surface acreage (by land area) in 2010 with 25.9% coverage (6,592 acres). The second largest percentage was the Hampton Harbor unit, 24.6% (2,980 acres) while the third largest unit was Cocheco River unit estimated at 19.8% (3,115 acres). As would be expected, the rural subwatersheds such as Branch Brook exhibited the lowest amounts of impervious surface area.

Tables 6 and 7 report on impervious surface acreage by state and town within the project area, for each of the 4 reporting intervals (1990, 2000, 2005, and 2010).

Associated with satellite image based mapping, error matrices are used to report the approximate accuracy of the results.  Typically, the matrix presents classified data results (e.g. derived from image processing) relative to reference data (e.g. data acquired via field visits or from some other source of known reliability).   While the assessments for this project utilized the standard assessment technique, the methodology cannot fully characterize the reliability of our results because the impervious surface pixels were mapped on a percentage basis.  The accuracy assessment only evaluated the presence/absence of imperviousness at a given site, not the percentage impervious.

With this caveat, error matrices are presented in Table 8. The table shows an overall accuracy for this time step of 95.5%.  A User’s Accuracy of 93.0% and 98.0% was achieved for Impervious and Non impervious features. Likewise, percentages of 97.9% and 93.3% resulted for the Producer’s accuracy (Impervious and Non impervious). By constraining our accuracy assessment selection technique, the site selections were probably biased in favor of those areas that are most easily mapped (e.g. large parking lots, buildings, and residential subdivisions rather than single houses and isolated features).  Nevertheless, the assessments provide a general estimate of the data reliability.

.

Note:  Acreages based on 1:24,000-scale town boundary and surface water data, both retrieved in December, 2008 from the Maine GIS Data Catalog (http://megis.maine.gov/catalog).  The total area of the coastal towns includes significant water acreage (as legal town bounds extend into the Atlantic Ocean).

Note:  Minor differences in total impervious acreage estimates (e.g. < 20 acres) reported at the town vs. subwatershed levels result from discrepancies in coastline delineations between the two data sets.

## References

Justice, D. and Rubin, F.  2006.  Final Report:  Impervious Surface Mapping in Coastal New Hampshire (2005).  24 p.

Justice, D. and Rubin, F.  2003.  Final Report:  Developing Impervious Surface Estimates for Coastal New Hampshire.  25 p.

# Text boxes

###### Figure 1. Project area.

###### Figure 2.  Regional mapping of impervious surfaces, 1990.   Impervious surface features are shown in red, and are displayed on the 12-digit watershed units.

###### Figure 3.  Regional mapping of impervious surfaces, 2000.   Impervious surface features are shown in red, and are displayed on the 12-digit watershed units.

###### Figure 4.  Regional mapping of impervious surfaces, 2005.   Impervious surface features are shown in red, and are displayed on the 12-digit watershed units.

###### Figure 5.  Regional mapping of impervious surfaces, 2010.   Impervious surface

###### features are shown in red, and are displayed on the 12-digit watershed units.

###### Figure 6. Regional mapping of impervious surfaces, 1990, for the York, ME vicinity.

###### Figure 7. Regional mapping of impervious surfaces, 2000 for the York, ME vicinity.

Figure 8. Regional mapping of impervious surfaces, 2005, for the York, ME vicinity.

Figure 9. Regional mapping of impervious surfaces, 2005, for the York, ME vicinity.

###### Table 1. Impervious surface acreage and total acreage by subwatershed, 1990.

Table 1 (cont.). Impervious surface acreage and total acreage by subwatershed, 1990.

###### Table 2. Impervious surface acreage and total acreage by subwatershed, 2000.

Table 2 (cont.). Impervious surface acreage and total acreage by subwatershed, 2000

###### Table 3. Impervious surface acreage and total acreage by subwatershed, 2005.

Table 3 (cont.). Impervious surface acreage and total acreage by subwatershed, 2005.

###### Table 4. Impervious surface acreage and total acreage by subwatershed, 2010.

Table 4 (cont.). Impervious surface acreage and total acreage by subwatershed, 2010.

###### Table 5. Impervious surface acreage change by subwatershed: 1990 – 2010.

###### Table 5 (cont.). Impervious surface acreage change by subwatershed: 1990 – 2010.

###### Table 6. Impervious surface acreage for towns in Maine.

###### Table 7. Impervious surface acreage for towns in New Hampshire.

Table 7 (cont.). Impervious surface acreage for towns in New Hampshire.

###### Table 8.  Accuracy assessment error matrix, 2010.