|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Blackwater River |  |  |  |  |  |  |  |  |  |
|  | A | 1,300 | 90 | 1,659 | 1.80 | 359.7 | 359.32 | 360.3 | 1.0 |  |
|  | B | 2,850 | 158 | 1,962 | 1.50 | 359.7 | 359.42 | 360.4 | 1.0 |  |
|  | C | 4,910 | 85 | 1,639 | 1.80 | 359.7 | 359.62 | 360.6 | 1.0 |  |
|  | D | 6,730 | 614 | 6,406 | 0.50 | 359.7 | 359.72 | 360.7 | 1.0 |  |
|  | E | 8,110 | 457 | 4,781 | 0.60 | 359.7 | 359.72 | 360.7 | 1.0 |  |
|  | F | 10,435 | 44 | 527 | 13.90 | 362.3 | 362.3 | 362.3 | 0.0 |  |
|  | G | 10,493 | 250 | 1,895 | 1.40 | 362.3 | 362.3 | 362.3 | 0.0 |  |
|  | H | 11,660 | 140 | 1,601 | 1.60 | 362.4 | 362.4 | 362.4 | 0.0 |  |
|  | I | 15,260 | 150 | 1,561 | 1.70 | 362.7 | 362.7 | 362.7 | 0.0 |  |
|  | J | 18,260 | 135 | 1,365 | 1.90 | 362.9 | 362.9 | 363.0 | 0.1 |  |
|  | K | 20,460 | 193 | 1,533 | 1.70 | 363.3 | 363.3 | 363.5 | 0.2 |  |
|  | L | 24,260 | 178 | 1,447 | 1.80 | 364.4 | 364.4 | 364.7 | 0.3 |  |
|  | M | 29,060 | 209 | 1,550 | 1.70 | 365.9 | 365.9 | 366.4 | 0.5 |  |
|  | N | 31,460 | 55 | 731 | 3.60 | 367.1 | 367.1 | 367.6 | 0.5 |  |
|  | O | 31,520 | 133 | 927 | 2.80 | 367.1 | 367.1 | 367.6 | 0.5 |  |
|  | P | 32,960 | 153 | 319 | 8.20 | 383.1 | 383.1 | 383.1 | 0.0 |  |
|  | Q | 34,660 | 173 | 633 | 4.10 | 408.0 | 408.0 | 408.0 | 0.0 |  |
|  | R | 36,560 | 108 | 295 | 8.80 | 423.9 | 423.9 | 423.9 | 0.0 |  |
|  | S | 37,735 | 41 | 261 | 10.00 | 435.4 | 435.4 | 435.7 | 0.3 |  |
|  | T | 41,560 | 57 | 560 | 4.40 | 444.8 | 444.8 | 445.3 | 0.5 |  |
|  | U | 41,608 | 84 | 666 | 3.90 | 445.1 | 445.1 | 445.7 | 0.6 |  |
|  | V | 44,160 | 86 | 266 | 9.80 | 460.5 | 460.5 | 460.5 | 0.0 |  |
|  | W | 48,085 | 83 | 846 | 3.10 | 470.7 | 470.7 | 471.5 | 0.8 |  |
|  | X | 50,285 | 82 | 707 | 3.70 | 471.8 | 471.8 | 472.6 | 0.8 |  |
|  | 1Feet above confluence with Contoocook River 2Elevation computed without consideration of backwater effects from Contoocook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | BLACKWATER RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Chance Pond Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.0301 | 16 | 59 | 11.00 | 290.0 | 290.0 | 290.4 | 0.4 |  |
|  | B | 0.2061 | 25 | 173 | 3.80 | 364.9 | 364.9 | 365.0 | 0.1 |  |
|  | C | 0.4971 | 20 | 64 | 10.20 | 373.0 | 373.0 | 373.0 | 0.0 |  |
|  | D | 0.7631 | 175 | 1,587 | 0.40 | 399.4 | 399.4 | 400.4 | 1.0 |  |
|  | E | 1.1081 | 230 | 1,613 | 0.40 | 399.4 | 399.4 | 400.4 | 1.0 |  |
|  | F | 1.5941 | 54 | 353 | 1.90 | 403.3 | 403.3 | 403.6 | 0.3 |  |
|  | Contoocook River |  |  |  |  |  |  |  |  |  |
|  | A | 100.7352 | 1,075 | 6,165 | 3.80 | 253.7 | 249.93 | 250.9 | 1.0 |  |
|  | B | 101.0682 | 570 | 2,965 | 7.90 | 271.5 | 271.5 | 271.5 | 0.0 |  |
|  | C | 101.3032 | 390 | 3,025 | 7.70 | 286.7 | 286.7 | 287.3 | 0.6 |  |
|  | D | 101.6802 | 160 | 3,055 | 7.60 | 307.8 | 307.8 | 308.1 | 0.3 |  |
|  | E | 102.1402 | 220 | 1,927 | 10.20 | 311.2 | 311.2 | 311.7 | 0.5 |  |
|  | F | 103.3302 | 300 | 5,917 | 3.90 | 353.2 | 353.2 | 353.4 | 0.2 |  |
|  | G | 104.0402 | 230 | 4,569 | 5.10 | 354.2 | 354.2 | 354.5 | 0.3 |  |
|  | H | 104.5802 | 225 | 4,575 | 5.10 | 355.6 | 355.6 | 355.9 | 0.3 |  |
|  | I | 105.1302 | 250 | 4,931 | 4.70 | 356.3 | 356.3 | 356.6 | 0.3 |  |
|  | J | 106.1102 | 230 | 4,963 | 4.70 | 357.2 | 357.2 | 357.5 | 0.3 |  |
|  | K | 107.8602 | 735 | 4,013 | 5.80 | 357.9 | 357.9 | 358.8 | 0.9 |  |
|  | L | 108.5102 | 515 | 6,287 | 3.70 | 358.8 | 358.8 | 359.5 | 0.7 |  |
|  | M | 108.8092 | 667 | 12,757 | 1.80 | 359.2 | 359.2 | 360.0 | 0.8 |  |
|  | N | 108.9422 | 221 | 4,712 | 4.90 | 359.2 | 359.2 | 360.0 | 0.8 |  |
|  | O | 109.2182 | 853 | 11,051 | 2.10 | 359.5 | 359.5 | 360.3 | 0.8 |  |
|  | P | 109.5902 | 850 | 8,789 | 2.70 | 359.7 | 359.7 | 360.5 | 0.8 |  |
|  | Q | 109.7922 | 1,100 | 12,941 | 1.50 | 359.9 | 359.9 | 360.8 | 0.9 |  |
|  | R | 110.1692 | 1,405 | 10,845 | 1.80 | 360.0 | 360.0 | 360.9 | 0.9 |  |
|  | ¹Miles above confluence with Pemigewasset River 2Miles above Newburyport Light, Newburyport, MA 3Elevation computed without consideration of backwater effects from Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | CHANCE POND BROOK – CONTOOCOOK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Contoocook River (continued) |  |  |  |  |  |  |  |  |  |
|  | S | 110.3781 | 737 | 7,135 | 2.70 | 360.0 | 360.0 | 360.9 | 0.9 |  |
|  | T | 110.8831 | 221 | 5,091 | 3.80 | 360.6 | 360.6 | 361.5 | 0.9 |  |
|  | U | 111.3951 | 494 | 6,048 | 3.20 | 361.0 | 361.0 | 361.9 | 0.9 |  |
|  | V | 111.9481 | 230 | 4,850 | 4.00 | 361.3 | 361.3 | 362.3 | 1.0 |  |
|  | W | 112.3721 | 740 | 7,413 | 2.60 | 361.8 | 361.8 | 362.7 | 0.9 |  |
|  | X | 112.9871 | 984 | 9,856 | 1.00 | 362.1 | 362.1 | 363.1 | 1.0 |  |
|  | Y | 113.5631 | 216 | 3,162 | 3.00 | 362.6 | 362.6 | 363.5 | 0.9 |  |
|  | Z | 113.8101 | 168 | 2,602 | 3.70 | 363.6 | 363.6 | 364.4 | 0.8 |  |
|  | AA | 114.0331 | 210 | 3,557 | 2.70 | 364.0 | 364.0 | 364.7 | 0.7 |  |
|  | AB | 114.6961 | 240 | 3,435 | 2.80 | 364.8 | 364.8 | 365.5 | 0.7 |  |
|  | AC | 114.8951 | 536 | 5,505 | 1.70 | 364.9 | 364.9 | 365.7 | 0.8 |  |
|  | AD | 115.7391 | 1,050 | 6,590 | 1.40 | 365.1 | 365.1 | 366.0 | 0.9 |  |
|  | AE | 116.6731 | 1,182 | 7,078 | 1.30 | 365.3 | 365.3 | 366.3 | 1.0 |  |
|  | AF | 117.1281 | 407 | 4,291 | 2.20 | 365.5 | 365.5 | 366.5 | 1.0 |  |
|  | AG | 117.6241 | 912 | 6,996 | 1.40 | 365.8 | 365.8 | 366.8 | 1.0 |  |
|  | AH | 118.1201 | 294 | 3,004 | 3.20 | 366.1 | 366.1 | 367.1 | 1.0 |  |
|  | AI | 118.6111 | 430 | 4,104 | 2.30 | 366.6 | 366.6 | 367.6 | 1.0 |  |
|  | AJ | 119.0211 | 100 | 865 | 11.00 | 367.0 | 367.0 | 367.9 | 0.9 |  |
|  | AK | 119.3741 | 477 | 7,731 | 1.20 | 382.8 | 382.8 | 383.1 | 0.3 |  |
|  | AL | 0.0902 | 204 | 3,792 | 5.70 | 421.8 | 421.8 | 421.8 | 0.0 |  |
|  | AM | 0.1802 | 229 | 4,062 | 5.32 | 423.4 | 423.4 | 423.4 | 0.0 |  |
|  | AN | 0.4202 | 316 | 4,957 | 4.36 | 423.9 | 423.9 | 424.0 | 0.1 |  |
|  | AO | 0.6602 | 200 | 2,408 | 8.97 | 423.9 | 423.9 | 423.9 | 0.0 |  |
|  | AP | 0.7502 | 184 | 2,980 | 7.25 | 425.0 | 425.0 | 425.3 | 0.3 |  |
|  | AQ | 1.0102 | 178 | 3,264 | 6.62 | 427.6 | 427.6 | 427.7 | 0.1 |  |
|  | AR | 1.2602 | 320 | 5,759 | 3.75 | 428.1 | 428.1 | 428.6 | 0.5 |  |
|  | 1Miles above Newburyport Light, Newburyport, MA 2Miles above State Route 114 |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | CONTOOCOOK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Contoocook River (continued) |  |  |  |  |  |  |  |  |  |
|  | AS | 1.4701 | 219 | 3,392 | 6.37 | 428.1 | 428.1 | 428.7 | 0.6 |  |
|  | AT | 1.5801 | 212 | 2,471 | 8.74 | 431.0 | 431.0 | 431.0 | 0.0 |  |
|  | AU | 1.6701 | 236 | 2,171 | 9.95 | 431.8 | 431.8 | 432.5 | 0.7 |  |
|  | AV | 1.7001 | 323 | 2,233 | 9.67 | 438.3 | 438.3 | 438.3 | 0.0 |  |
|  | AW | 1.9601 | 313 | 5,218 | 4.14 | 440.9 | 440.9 | 440.9 | 0.0 |  |
|  | AX | 2.1501 | 209 | 2,434 | 8.88 | 440.9 | 440.9 | 440.9 | 0.0 |  |
|  | AY | 2.4001 | 180 | 1,388 | 15.56 | 451.0 | 451.0 | 451.1 | 0.1 |  |
|  | AZ | 2.6201 | 242 | 1,985 | 10.88 | 464.5 | 464.5 | 464.5 | 0.0 |  |
|  | BA | 2.7901 | 306 | 2,469 | 8.75 | 471.6 | 471.6 | 471.7 | 0.1 |  |
|  | BB | 3.2401 | 215 | 2,784 | 7.76 | 491.1 | 491.1 | 491.1 | 0.0 |  |
|  | BC | 3.8201 | 244 | 2,353 | 9.18 | 522.2 | 522.2 | 522.2 | 0.0 |  |
|  | BD | 4.0901 | 158 | 1,546 | 13.97 | 538.0 | 538.0 | 538.0 | 0.0 |  |
|  | BE | 4.4201 | 186 | 1,570 | 13.76 | 550.4 | 550.4 | 550.4 | 0.0 |  |
|  | Dalton Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.0202 | 10 | 41 | 8.30 | 186.7 | 182.43 | 182.4 | 0.0 |  |
|  | B | 0.6002 | 35 | 99 | 3.40 | 241.7 | 241.7 | 242.3 | 0.6 |  |
|  | C | 1.2102 | 20 | 43 | 6.00 | 289.8 | 289.8 | 290.0 | 0.2 |  |
|  | D | 1.3162 | 25 | 79 | 3.30 | 294.6 | 294.6 | 295.0 | 0.4 |  |
|  | E | 1.4092 | 8 | 45 | 5.80 | 297.6 | 297.6 | 297.7 | 0.1 |  |
|  | Glines Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.1242 | 30 | 250 | 2.40 | 264.5 | 260.73 | 261.7 | 1.0 |  |
|  | B | 0.2452 | 20 | 65 | 9.10 | 284.5 | 284.5 | 284.7 | 0.2 |  |
|  | 1Miles above State Route 114 2Miles above confluence with Merrimack River 3Elevation computed without consideration of backwater effects from Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | CONTOOCOOK RIVER – DALTON BROOK – GLINES BROOK |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Little Suncook River |  |  |  |  |  |  |  |  |  |
|  | A | 0.000 | 766 | 1,361 | 1.20 | 338.4 | 326.02 | 326.9 | 0.9 |  |
|  | B | 0.070 | 800 | 3,899 | 0.40 | 338.4 | 333.82 | 333.9 | 0.1 |  |
|  | C | 0.380 | 48 | 159 | 10.44 | 339.5 | 339.5 | 340.0 | 0.5 |  |
|  | D | 0.470 | 49 | 208 | 7.98 | 344.1 | 344.1 | 345.1 | 1.0 |  |
|  | E | 0.510 | 49 | 295 | 5.63 | 346.7 | 346.7 | 346.9 | 0.2 |  |
|  | F | 0.640 | 51 | 174 | 9.54 | 349.9 | 349.9 | 350.1 | 0.2 |  |
|  | G | 0.770 | 60 | 280 | 5.93 | 356.7 | 356.7 | 356.7 | 0.0 |  |
|  | H | 0.920 | 53 | 176 | 8.47 | 362.0 | 362.0 | 362.2 | 0.2 |  |
|  | I | 1.050 | 65 | 271 | 5.50 | 370.0 | 370.0 | 370.0 | 0.0 |  |
|  | J | 1.130 | 57 | 157 | 9.49 | 377.6 | 377.6 | 377.6 | 0.0 |  |
|  | K | 1.320 | 79 | 301 | 4.95 | 388.9 | 388.9 | 389.0 | 0.1 |  |
|  | L | 1.420 | 80 | 175 | 8.51 | 394.4 | 394.4 | 394.4 | 0.0 |  |
|  | M | 1.480 | 67 | 187 | 7.97 | 398.3 | 398.3 | 398.5 | 0.2 |  |
|  | N | 1.640 | 28 | 190 | 7.84 | 408.8 | 408.8 | 409.0 | 0.2 |  |
|  | O | 1.720 | 128 | 518 | 2.88 | 410.9 | 410.9 | 411.2 | 0.3 |  |
|  | P | 1.760 | 190 | 701 | 2.13 | 411.5 | 411.5 | 411.8 | 0.3 |  |
|  | Q | 1.880 | 45 | 234 | 6.37 | 415.5 | 415.5 | 416.4 | 0.9 |  |
|  | R | 2.020 | 77 | 221 | 6.74 | 424.5 | 424.5 | 424.5 | 0.0 |  |
|  | S | 2.100 | 83 | 242 | 6.16 | 429.8 | 429.8 | 429.9 | 0.1 |  |
|  | T | 2.150 | 90 | 943 | 1.58 | 436.7 | 436.7 | 436.7 | 0.0 |  |
|  | U | 2.490 | 58 | 144 | 9.06 | 439.5 | 439.5 | 439.5 | 0.0 |  |
|  | V | 2.600 | 66 | 299 | 3.23 | 442.8 | 442.8 | 443.1 | 0.3 |  |
|  | W | 2.760 | 284 | 1,045 | 0.92 | 443.5 | 443.5 | 444.2 | 0.7 |  |
|  | X | 3.000 | 36 | 121 | 7.98 | 444.8 | 444.8 | 445.4 | 0.6 |  |
|  | Y | 3.230 | 55 | 210 | 4.60 | 460.7 | 460.7 | 461.1 | 0.4 |  |
|  | ¹Miles above confluence with Suncook River 2Elevation computed without consideration of backwater effects from Suncook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | LITTLE SUNCOOK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Little Suncook River (continued) |  |  |  |  |  |  |  |  |  |
|  | Z | 3.3501 | 64 | 123 | 7.85 | 473.2 | 473.2 | 473.4 | 0.2 |  |
|  | AA | 3.4401 | 50 | 165 | 5.85 | 482.4 | 482.4 | 482.9 | 0.5 |  |
|  | AB | 3.5501 | 39 | 103 | 9.37 | 504.9 | 504.9 | 504.9 | 0.0 |  |
|  | AC | 3.6201 | 236 | 1,270 | 0.76 | 518.7 | 518.7 | 518.7 | 0.0 |  |
|  | Merrimack River |  |  |  |  |  |  |  |  |  |
|  | A | 76.3902 | 4353 | 10,854 | 6.00 | 184.7 | 184.7 | 185.2 | 0.5 |  |
|  | B | 77.4432 | 520 | 10,896 | 6.00 | 186.6 | 186.6 | 187.0 | 0.4 |  |
|  | C | 78.7252 | 520 | 13,565 | 4.50 | 189.0 | 189.0 | 189.3 | 0.3 |  |
|  | D | 80.5002 | 390 | 11,679 | 5.20 | 190.4 | 190.4 | 190.7 | 0.3 |  |
|  | E | 80.9602 | 450 | 11,235 | 5.00 | 191.4 | 191.4 | 191.6 | 0.2 |  |
|  | F | 82.2572 | 635 | 10,512 | 5.30 | 197.1 | 197.1 | 197.4 | 0.3 |  |
|  | G | 82.9832 | 602 | 10,624 | 5.20 | 198.0 | 198.0 | 198.3 | 0.3 |  |
|  | H | 84.4982 | 562 | 10,288 | 5.40 | 200.2 | 200.2 | 200.4 | 0.2 |  |
|  | I | 85.3962 | 247 | 5,510 | 10.10 | 201.4 | 201.4 | 201.5 | 0.1 |  |
|  | J | 85.8762 | 798 | 14,217 | 3.90 | 203.3 | 203.3 | 203.5 | 0.2 |  |
|  | K | 86.5232 | 617 | 13,624 | 4.10 | 203.7 | 203.7 | 203.9 | 0.2 |  |
|  | L | 86.7852 | 612 | 8,379 | 5.50 | 224.2 | 224.2 | 224.2 | 0.0 |  |
|  | M | 87.3062 | 602 | 10,335 | 4.50 | 225.6 | 225.6 | 225.6 | 0.0 |  |
|  | N | 87.7952 | 436 | 5,411 | 8.50 | 226.1 | 226.1 | 226.1 | 0.0 |  |
|  | O | 88.1382 | 509 | 8,827 | 5.20 | 227.7 | 227.7 | 227.7 | 0.0 |  |
|  | P | 88.8732 | 575 | 10,815 | 4.30 | 229.1 | 229.1 | 229.1 | 0.0 |  |
|  | Q | 89.9632 | 482 | 8,910 | 5.20 | 230.2 | 230.2 | 230.2 | 0.0 |  |
|  | R | 90.4712 | 661 | 11,182 | 4.10 | 231.0 | 231.0 | 231.0 | 0.0 |  |
|  | S | 91.5312 | 506 | 10,400 | 4.20 | 231.9 | 231.9 | 232.3 | 0.4 |  |
|  | 1Miles above confluence with Suncook River 2Miles above confluence with Newburyport Light, Newburyport, MA 3This width extends beyond the county boundary |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | LITTLE SUNCOOK RIVER – MERRIMACK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Merrimack River (continued) |  |  |  |  |  |  |  |  |  |
|  | T | 91.651 | 493 | 10,022 | 4.40 | 232.0 | 232.0 | 232.4 | 0.4 |  |
|  | U | 92.418 | 475 | 10,303 | 4.30 | 232.7 | 232.7 | 233.1 | 0.4 |  |
|  | V | 92.815 | 371 | 8,984 | 4.90 | 233.2 | 233.2 | 233.4 | 0.2 |  |
|  | W | 93.092 | 2,072 | 24,679 | 1.80 | 233.3 | 233.3 | 233.8 | 0.5 |  |
|  | X | 93.878 | 514 | 10,326 | 4.30 | 233.6 | 233.6 | 234.3 | 0.7 |  |
|  | Y | 94.230 | 429 | 9,647 | 4.60 | 234.0 | 234.0 | 234.5 | 0.5 |  |
|  | Z | 95.624 | 543 | 8,645 | 5.10 | 235.2 | 235.2 | 235.9 | 0.7 |  |
|  | AA | 97.140 | 685 | 7,311 | 6.00 | 237.8 | 237.8 | 238.4 | 0.6 |  |
|  | AB | 98.112 | 389 | 4,134 | 10.60 | 241.4 | 241.4 | 241.6 | 0.2 |  |
|  | AC | 98.640 | 363 | 4,606 | 9.60 | 246.2 | 246.2 | 246.2 | 0.0 |  |
|  | AD | 98.684 | 352 | 4,807 | 9.20 | 247.2 | 247.2 | 247.2 | 0.0 |  |
|  | AE | 99.805 | 440 | 8,873 | 5.00 | 250.2 | 250.2 | 250.4 | 0.2 |  |
|  | AF | 100.992 | 435 | 9,710 | 3.90 | 253.9 | 253.9 | 254.8 | 0.9 |  |
|  | AG | 101.898 | 930 | 11,935 | 3.20 | 254.9 | 254.9 | 255.7 | 0.8 |  |
|  | AH | 102.870 | 490 | 6,990 | 5.40 | 256.3 | 256.3 | 257.2 | 0.9 |  |
|  | AI | 104.290 | 730 | 12,785 | 3.00 | 258.6 | 258.6 | 259.5 | 0.9 |  |
|  | AJ | 105.070 | 290 | 7,175 | 5.30 | 259.3 | 259.3 | 260.2 | 0.9 |  |
|  | AK | 106.760 | 1,170 | 18,860 | 2.00 | 261.2 | 261.2 | 262.1 | 0.9 |  |
|  | AL | 108.130 | 250 | 6,135 | 6.20 | 262.4 | 262.4 | 263.3 | 0.9 |  |
|  | AM | 108.760 | 275 | 6,625 | 5.70 | 263.6 | 263.6 | 264.6 | 1.0 |  |
|  | AN | 110.250 | 705 | 9,310 | 4.10 | 266.1 | 266.1 | 267.1 | 1.0 |  |
|  | AO | 111.370 | 290 | 7,595 | 5.00 | 267.3 | 267.3 | 268.3 | 1.0 |  |
|  | AP | 112.160 | 715 | 10,599 | 3.00 | 268.3 | 268.3 | 269.2 | 0.9 |  |
|  | AQ | 113.000 | 325 | 9,230 | 3.40 | 268.8 | 268.8 | 269.8 | 1.0 |  |
|  | AR | 113.560 | 726 | 11,775 | 2.70 | 269.2 | 269.2 | 270.1 | 0.9 |  |
|  | AS | 114.780 | 260 | 6,109 | 5.10 | 269.9 | 269.9 | 270.9 | 1.0 |  |
|  | ¹ Miles above confluence with Newburyport Light, Newburyport, MA |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | MERRIMACK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Messer Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.0241 | 12 | 84 | 6.80 | 185.6 | 179.04 | 179.0 | 0.0 |  |
|  | B | 0.1741 | 20 | 124 | 4.60 | 196.8 | 196.8 | 196.8 | 0.0 |  |
|  | C | 0.6551 | 20 | 56 | 8.20 | 220.2 | 220.2 | 220.2 | 0.0 |  |
|  | D | 0.9751 | 8 | 37 | 12.40 | 233.2 | 233.2 | 233.6 | 0.4 |  |
|  | E | 1.2551 | 12 | 48 | 9.60 | 258.2 | 258.2 | 258.2 | 0.0 |  |
|  | Pemigewasset River |  |  |  |  |  |  |  |  |  |
|  | A | 116.2452 | 247 | 2,789 | 7.90 | 273.0 | 273.0 | 273.7 | 0.7 |  |
|  | B | 116.5902 | 180 | 1,465 | 15.00 | 278.4 | 278.4 | 278.4 | 0.0 |  |
|  | C | 117.2002 | 319 | 6,405 | 3.40 | 308.2 | 308.2 | 308.2 | 0.0 |  |
|  | Peters Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.3741 | 30 | 161 | 3.90 | 222.5 | 222.5 | 222.5 | 0.0 |  |
|  | B | 0.7701 | 10 | 50 | 12.50 | 253.9 | 253.9 | 254.2 | 0.3 |  |
|  | C | 0.9101 | 20 | 180 | 3.50 | 278.2 | 278.2 | 278.7 | 0.5 |  |
|  | D | 1.0701 | 20 | 98 | 4.10 | 287.9 | 287.9 | 287.9 | 0.0 |  |
|  | E | 1.2851 | 17 | 130 | 3.10 | 293.5 | 293.5 | 294.0 | 0.5 |  |
|  | F | 1.7051 | 45 | 81 | 5.00 | 301.2 | 301.2 | 301.3 | 0.1 |  |
|  | Sanders Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.0503 | 36 | 371 | 1.06 | 343.0 | 341.75 | 342.3 | 0.6 |  |
|  | B | 0.1203 | 36 | 307 | 1.29 | 343.0 | 341.75 | 342.4 | 0.7 |  |
|  | C | 0.2403 | 37 | 137 | 2.88 | 349.4 | 349.4 | 349.5 | 0.1 |  |
|  | D | 0.3303 | 27 | 60 | 6.58 | 352.7 | 352.7 | 353.3 | 0.6 |  |
|  | 1Miles above confluence with Merrimack River 4Elevation computed without consideration of backwater effects from Merrimack River 2Miles above Newburyport Light, Newburyport, MA 5Elevation computed without consideration of backwater effects from Suncook River 3Miles above confluence with Suncook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | MESSER BROOK – PEMIGEWASSET RIVER – PETERS BROOK – SANDERS BROOK |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Soucook River |  |  |  |  |  |  |  |  |  |
|  | A | 0.350 | 295 | 2,660 | 2.10 | 203.4 | 203.12 | 204.1 | 1.0 |  |
|  | B | 1.165 | 100 | 960 | 5.90 | 205.8 | 205.8 | 206.3 | 0.5 |  |
|  | C | 4.116 | 265 | 1,623 | 3.40 | 229.2 | 229.2 | 229.4 | 0.2 |  |
|  | D | 6.665 | 70 | 454 | 12.20 | 248.3 | 248.3 | 248.3 | 0.0 |  |
|  | E | 7.582 | 105 | 1,129 | 4.90 | 261.4 | 261.4 | 262.2 | 0.8 |  |
|  | F | 9.032 | 200 | 1,603 | 3.30 | 270.4 | 270.4 | 271.1 | 0.7 |  |
|  | G | 12.213 | 75 | 1,027 | 5.10 | 303.5 | 303.5 | 304.3 | 0.8 |  |
|  | Suncook River |  |  |  |  |  |  |  |  |  |
|  | A | 0.050 | 265 | 3,236 | 4.70 | 197.9 | 197.9 | 198.9 | 1.0 |  |
|  | B | 0.439 | 207 | 3,877 | 3.90 | 236.7 | 236.7 | 236.7 | 0.0 |  |
|  | C | 0.564 | 87 | 2,744 | 5.50 | 261.1 | 261.1 | 261.1 | 0.0 |  |
|  | D | 0.847 | 252 | 4,126 | 3.70 | 283.7 | 283.7 | 283.8 | 0.1 |  |
|  | E | 1.186 | 142 | 1,747 | 8.70 | 285.5 | 285.5 | 285.8 | 0.3 |  |
|  | F | 1.654 | 192 | 3,165 | 4.80 | 288.3 | 288.3 | 288.6 | 0.3 |  |
|  | G | 2.010 | 221 | 2,665 | 5.60 | 289.2 | 289.2 | 289.4 | 0.2 |  |
|  | H | 2.995 | 1,041 | 9,953 | 1.50 | 290.5 | 290.5 | 291.3 | 0.8 |  |
|  | I | 4.137 | 980 | 10,142 | 1.40 | 292.8 | 292.8 | 293.8 | 1.0 |  |
|  | J | 4.785 | 1,235 | 9,024 | 1.60 | 293.4 | 293.4 | 294.4 | 1.0 |  |
|  | K | 5.490 | 322 | 2,584 | 5.60 | 299.0 | 299.0 | 299.0 | 0.0 |  |
|  | L | 5.525 | 287 | 4,472 | 3.20 | 301.4 | 301.4 | 301.4 | 0.0 |  |
|  | M | 5.570 | 147 | 3,015 | 4.80 | 301.5 | 301.5 | 301.6 | 0.1 |  |
|  | N | 6.330 | 230 | 3,864 | 3.70 | 302.9 | 302.9 | 303.5 | 0.6 |  |
|  | O | 6.667 | 155 | 2,670 | 5.20 | 303.3 | 303.3 | 304.1 | 0.8 |  |
|  | P | 6.937 | 225 | 3,238 | 4.30 | 304.3 | 304.3 | 305.3 | 1.0 |  |
|  | Q | 7.035 | 626 | 6,817 | 3.72 | 304.5 | 304.5 | 305.5 | 1.0 |  |
|  | ¹Miles above confluence with Merrimack River 2Elevation computed without consideration of backwater effects from Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | SOUCOOK RIVER – SUNCOOK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Suncook River (continued) |  |  |  |  |  |  |  |  |  |
|  | R | 7.060 | 626 | 6,817 | 3.72 | 304.5 | 304.5 | 305.5 | 1.0 |  |
|  | S | 7.900 | 449 | 6,285 | 3.76 | 305.5 | 305.5 | 306.5 | 1.0 |  |
|  | T | 8.270 | 450 | 5,956 | 2.25 | 305.9 | 305.9 | 306.9 | 1.0 |  |
|  | U | 8.650 | 440 | 4,085 | 3.21 | 306.3 | 306.3 | 307.2 | 0.9 |  |
|  | V | 9.250 | 290 | 3,872 | 3.39 | 307.4 | 307.4 | 308.1 | 0.7 |  |
|  | W | 9.470 | 450 | 8,314 | 1.58 | 307.7 | 307.7 | 308.5 | 0.8 |  |
|  | X | 9.540 | 106 | 1,719 | 7.63 | 308.3 | 308.3 | 308.7 | 0.4 |  |
|  | Y | 9.580 | 129 | 1,855 | 7.07 | 308.9 | 308.9 | 309.3 | 0.4 |  |
|  | Z | 9.670 | 228 | 3,643 | 3.60 | 309.4 | 309.4 | 310.0 | 0.6 |  |
|  | AA | 10.080 | 600 | 7,766 | 1.65 | 309.7 | 309.7 | 310.4 | 0.7 |  |
|  | AB | 10.630 | 817 | 8,428 | 1.52 | 309.7 | 309.7 | 310.6 | 0.9 |  |
|  | AC | 10.720 | 900 | 8,891 | 1.44 | 309.7 | 309.7 | 310.6 | 0.9 |  |
|  | AD | 10.850 | 400 | 4,043 | 3.17 | 309.7 | 309.7 | 310.7 | 1.0 |  |
|  | AE | 11.030 | 215 | 2,146 | 5.97 | 310.0 | 310.0 | 311.0 | 1.0 |  |
|  | AF | 11.220 | 200 | 1,494 | 6.12 | 311.5 | 311.5 | 312.0 | 0.5 |  |
|  | AG | 11.410 | 148 | 1,313 | 6.96 | 313.0 | 313.0 | 314.0 | 1.0 |  |
|  | AH | 11.570 | 350 | 3,139 | 2.91 | 314.7 | 314.7 | 315.7 | 1.0 |  |
|  | AI | 11.660 | 88 | 587 | 15.57 | 320.4 | 320.4 | 320.4 | 0.0 |  |
|  | AJ | 11.760 | 116 | 1,309 | 6.98 | 325.4 | 325.4 | 325.9 | 0.5 |  |
|  | AK | 11.900 | 128 | 687 | 13.30 | 331.2 | 331.2 | 331.2 | 0.0 |  |
|  | AL | 11.970 | 135 | 1,390 | 6.58 | 335.0 | 335.0 | 335.0 | 0.0 |  |
|  | AM | 12.460 | 600 | 5,121 | 2.50 | 337.8 | 337.8 | 338.4 | 0.6 |  |
|  | AN | 12.870 | 506 | 3,880 | 2.75 | 338.6 | 338.6 | 339.3 | 0.7 |  |
|  | AO | 12.960 | 625 | 4,460 | 2.39 | 338.8 | 338.8 | 339.6 | 0.8 |  |
|  | AP | 13.010 | 625 | 4,869 | 2.19 | 339.4 | 339.4 | 340.3 | 0.9 |  |
|  | AQ | 13.620 | 630 | 3,935 | 2.71 | 340.4 | 340.4 | 341.4 | 1.0 |  |
|  | ¹Miles above confluence with Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | SUNCOOK RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Suncook River (continued) |  |  |  |  |  |  |  |  |  |
|  | AR | 13.930 | 190 | 2,338 | 4.56 | 341.2 | 341.2 | 342.2 | 1.0 |  |
|  | AS | 14.910 | 880 | 8,999 | 1.18 | 342.9 | 342.9 | 343.8 | 0.9 |  |
|  | AT | 15.330 | 550 | 5,118 | 2.08 | 343.2 | 343.2 | 344.1 | 0.9 |  |
|  | AU | 15.700 | 171 | 1,535 | 6.73 | 343.7 | 343.7 | 344.5 | 0.8 |  |
|  | AV | 15.840 | 105 | 1,665 | 6.20 | 345.4 | 345.4 | 345.8 | 0.4 |  |
|  | AW | 16.110 | 175 | 2,249 | 4.59 | 345.9 | 345.9 | 346.7 | 0.8 |  |
|  | AX | 16.230 | 361 | 3,601 | 2.87 | 346.2 | 346.2 | 346.9 | 0.7 |  |
|  | AY | 16.640 | 700 | 5,050 | 2.05 | 346.7 | 346.7 | 347.7 | 1.0 |  |
|  | AZ | 16.800 | 900 | 6,011 | 1.62 | 346.9 | 346.9 | 347.9 | 1.0 |  |
|  | BA | 16.980 | 900 | 2,495 | 3.91 | 348.6 | 348.6 | 349.1 | 0.5 |  |
|  | BB | 17.140 | 950 | 2,978 | 3.27 | 352.6 | 352.6 | 352.7 | 0.1 |  |
|  | BC | 17.370 | 142 | 886 | 11.00 | 360.5 | 360.5 | 361.3 | 0.8 |  |
|  | BD | 17.690 | 160 | 1,240 | 7.86 | 375.5 | 375.5 | 375.7 | 0.2 |  |
|  | BE | 17.910 | 142 | 1,022 | 9.54 | 381.0 | 381.0 | 381.7 | 0.7 |  |
|  | BF | 18.140 | 181 | 926 | 10.53 | 391.6 | 391.6 | 391.6 | 0.0 |  |
|  | BG | 18.200 | 185 | 1,026 | 9.50 | 395.8 | 395.8 | 395.9 | 0.1 |  |
|  | BH | 18.260 | 138 | 816 | 11.95 | 399.4 | 399.4 | 399.6 | 0.2 |  |
|  | BI | 18.450 | 160 | 1,196 | 8.15 | 408.6 | 408.6 | 409.4 | 0.8 |  |
|  | BJ | 19.130 | 138 | 1,060 | 9.20 | 424.9 | 424.9 | 424.9 | 0.0 |  |
|  | BK | 19.530 | 115 | 1,260 | 7.74 | 430.5 | 430.5 | 431.2 | 0.7 |  |
|  | BL | 19.780 | 136 | 1,391 | 7.01 | 433.4 | 433.4 | 434.3 | 0.9 |  |
|  | BM | 19.970 | 110 | 1,127 | 8.65 | 435.7 | 435.7 | 436.6 | 0.9 |  |
|  | BN | 20.340 | 142 | 1,492 | 6.24 | 440.1 | 440.1 | 441.0 | 0.9 |  |
|  | BO | 20.700 | 126 | 1,175 | 7.92 | 443.8 | 443.8 | 444.2 | 0.4 |  |
|  | BP | 20.940 | 200 | 1,258 | 7.40 | 447.4 | 447.4 | 447.8 | 0.4 |  |
|  | BQ | 21.190 | 150 | 1,002 | 9.29 | 455.7 | 455.7 | 456.1 | 0.4 |  |
|  | ¹Miles above confluence with Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | SUNCOOK RIVER |
|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Suncook River (continued) |  |  |  |  |  |  |  |  |  |
|  | BR | 21.250 | 98 | 941 | 9.89 | 458.1 | 458.1 | 458.3 | 0.2 |  |
|  | BS | 21.330 | 368 | 5,546 | 1.68 | 480.1 | 480.1 | 480.1 | 0.0 |  |
|  | BT | 21.460 | 139 | 1,992 | 4.67 | 480.1 | 480.1 | 480.1 | 0.0 |  |
|  | BU | 21.490 | 138 | 1,935 | 4.81 | 480.1 | 480.1 | 480.1 | 0.0 |  |
|  | BV | 21.550 | 270 | 3,335 | 2.79 | 480.5 | 480.5 | 480.5 | 0.0 |  |
|  | BW | 21.940 | 468 | 5,849 | 1.59 | 480.7 | 480.7 | 480.7 | 0.0 |  |
|  | BX | 22.000 | 128 | 1,809 | 5.15 | 481.5 | 481.5 | 481.5 | 0.0 |  |
|  | BY | 22.390 | 135 | 1,658 | 5.62 | 482.2 | 482.2 | 482.3 | 0.1 |  |
|  | BZ | 22.560 | 170 | 1,277 | 7.29 | 482.2 | 482.2 | 482.8 | 0.6 |  |
|  | CA | 23.040 | 152 | 1,746 | 5.33 | 487.3 | 487.3 | 487.7 | 0.4 |  |
|  | CB | 23.410 | 161 | 1,896 | 4.91 | 488.6 | 488.6 | 489.3 | 0.7 |  |
|  | CC | 23.520 | 180 | 2,031 | 4.58 | 489.0 | 489.0 | 489.8 | 0.8 |  |
|  | Tannery Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.168 | 85 | 290 | 5.40 | 259.4 | 253.62 | 253.8 | 0.2 |  |
|  | B | 0.540 | 199 | 920 | 1.70 | 259.4 | 256.82 | 257.8 | 1.0 |  |
|  | C | 0.712 | 53 | 578 | 2.70 | 266.8 | 266.8 | 267.3 | 0.5 |  |
|  | D | 0.933 | 52 | 370 | 4.20 | 293.3 | 293.3 | 294.1 | 0.8 |  |
|  | E | 1.294 | 90 | 450 | 3.50 | 296.7 | 296.7 | 297.7 | 1.0 |  |
|  | F | 1.593 | 20 | 120 | 13.10 | 303.7 | 303.7 | 303.8 | 0.1 |  |
|  | G | 1.783 | 310 | 3,380 | 0.50 | 364.9 | 364.9 | 365.0 | 0.1 |  |
|  | H | 2.092 | 100 | 1,050 | 1.50 | 364.9 | 364.9 | 365.0 | 0.1 |  |
|  | I | 2.365 | 34 | 170 | 9.20 | 378.6 | 378.6 | 378.6 | 0.0 |  |
|  | J | 2.710 | 43 | 170 | 9.20 | 412.4 | 412.4 | 412.4 | 0.0 |  |
|  | K | 3.078 | 230 | 1,020 | 1.50 | 416.6 | 416.6 | 417.6 | 1.0 |  |
|  | ¹Miles above confluence with Merrimack River 2Elevation computed without consideration of backwater effects from Merrimack River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | SUNCOOK RIVER – TANNERY BROOK |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | The Outlet |  |  |  |  |  |  |  |  |  |
|  | A | 0.0001 | 300 | 3,438 | 1.10 | 309.8 | 309.8 | 310.2 | 0.4 |  |
|  | B | 0.2201 | 125 | 569 | 6.60 | 317.7 | 317.7 | 318.2 | 0.5 |  |
|  | C | 0.5401 | 80 | 696 | 5.40 | 321.5 | 321.5 | 322.0 | 0.5 |  |
|  | D | 0.6301 | 190 | 2,282 | 1.60 | 337.2 | 337.2 | 337.2 | 0.0 |  |
|  | E | 0.9601 | 75 | 709 | 5.30 | 346.5 | 346.5 | 346.7 | 0.2 |  |
|  | F | 1.2701 | 50 | 730 | 5.10 | 353.5 | 353.5 | 353.7 | 0.2 |  |
|  | Tioga River |  |  |  |  |  |  |  |  |  |
|  | A | 1.1652 | 76 | 485 | 7.50 | 471.7 | 471.7 | 472.5 | 0.8 |  |
|  | B | 1.7122 | 364 | 2,350 | 1.60 | 476.1 | 476.1 | 477.1 | 1.0 |  |
|  | Tributary A |  |  |  |  |  |  |  |  |  |
|  | A | 0.1753 | 10 | 30 | 12.30 | 256.2 | 250.25 | 250.2 | 0.0 |  |
|  | B | 0.4453 | 530 | 4,210 | 0.10 | 256.2 | 251.25 | 252.2 | 1.0 |  |
|  | C | 0.6673 | 25 | 50 | 7.40 | 256.2 | 252.65 | 253.1 | 0.5 |  |
|  | Warner River |  |  |  |  |  |  |  |  |  |
|  | A | 1,1404 | 96 | 1,070 | 9.10 | 361.5 | 355.16 | 355.8 | 0.7 |  |
|  | B | 2,3004 | 713 | 4,495 | 2.20 | 361.5 | 357.56 | 358.3 | 0.8 |  |
|  | C | 4,3604 | 388 | 2,442 | 4.00 | 361.5 | 358.86 | 359.4 | 0.6 |  |
|  | D | 8,1004 | 250 | 2,781 | 3.50 | 361.9 | 361.9 | 362.5 | 0.6 |  |
|  | E | 12,2404 | 308 | 3,305 | 2.90 | 363.4 | 363.4 | 364.1 | 0.7 |  |
|  | F | 13,0404 | 480 | 5,380 | 1.80 | 363.7 | 363.7 | 364.4 | 0.7 |  |
|  | G | 13,7904 | 254 | 750 | 12.70 | 371.1 | 371.1 | 371.1 | 0.0 |  |
|  | H | 14,0404 | 102 | 659 | 14.40 | 381.4 | 381.4 | 381.4 | 0.0 |  |
|  | I | 14,5654 | 106 | 1,265 | 7.50 | 392.5 | 392.5 | 392.5 | 0.0 |  |
|  | ¹Miles above confluence with Contoocook River 4Feet above confluence with Contoocook River 2Miles above confluence with Winnipesaukee River 5Elevation computed without consideration of backwater effects from Merrimack River 3Miles above confluence with Merrimack River 6Elevation computed without consideration of backwater effects from Contoocook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | THE OUTLET – TIOGA RIVER – TRIBUTARY A – WARNER RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Warner River (continued) |  |  |  |  |  |  |  |  |  |
|  | J | 16,310 | 400 | 3,512 | 2.70 | 393.7 | 393.7 | 393.9 | 0.2 |  |
|  | K | 18,740 | 550 | 5,079 | 1.90 | 394.5 | 394.5 | 395.1 | 0.6 |  |
|  | L | 21,440 | 399 | 3,490 | 2.70 | 394.5 | 394.5 | 395.5 | 1.0 |  |
|  | M | 21,990 | 200 | 2,423 | 3.90 | 395.4 | 395.4 | 396.0 | 0.6 |  |
|  | N | 22,170 | 350 | 2,693 | 3.50 | 395.4 | 395.4 | 396.1 | 0.7 |  |
|  | O | 23,910 | 1,050 | 9,907 | 1.00 | 396.0 | 396.0 | 396.7 | 0.7 |  |
|  | P | 26,550 | 684 | 4,195 | 2.30 | 396.3 | 396.3 | 397.1 | 0.8 |  |
|  | Q | 28,740 | 648 | 4,514 | 2.10 | 397.3 | 397.3 | 398.3 | 1.0 |  |
|  | R | 30,970 | 900 | 6,037 | 1.40 | 398.0 | 398.0 | 399.0 | 1.0 |  |
|  | S | 32,860 | 776 | 5,636 | 1.50 | 398.4 | 398.4 | 399.3 | 0.9 |  |
|  | T | 33,960 | 356 | 2,007 | 4.10 | 398.4 | 398.4 | 399.3 | 0.9 |  |
|  | U | 34,500 | 130 | 1,366 | 6.00 | 400.9 | 400.9 | 401.6 | 0.7 |  |
|  | V | 35,380 | 150 | 1,388 | 5.90 | 402.0 | 402.0 | 402.6 | 0.6 |  |
|  | W | 36,570 | 164 | 1,562 | 5.30 | 403.1 | 403.1 | 404.1 | 1.0 |  |
|  | X | 37,270 | 319 | 2,691 | 3.10 | 404.0 | 404.0 | 404.9 | 0.9 |  |
|  | Y | 37,592 | 200 | 1,744 | 4.70 | 405.0 | 405.0 | 405.3 | 0.3 |  |
|  | Z | 38,670 | 294 | 2,729 | 3.00 | 405.5 | 405.5 | 406.2 | 0.7 |  |
|  | AA | 38,936 | 111 | 1,311 | 6.30 | 405.5 | 405.5 | 406.2 | 0.7 |  |
|  | AB | 39,940 | 250 | 2,686 | 3.10 | 406.9 | 406.9 | 407.5 | 0.6 |  |
|  | AC | 41,740 | 500 | 3,516 | 2.30 | 407.8 | 407.8 | 408.8 | 1.0 |  |
|  | AD | 42,122 | 163 | 1,483 | 5.60 | 408.0 | 408.0 | 408.9 | 0.9 |  |
|  | AE | 42,980 | 350 | 2,877 | 2.90 | 409.2 | 409.2 | 409.8 | 0.6 |  |
|  | AF | 44,740 | 325 | 2,631 | 3.10 | 409.9 | 409.9 | 410.9 | 1.0 |  |
|  | AG | 45,035 | 170 | 1,718 | 4.80 | 410.6 | 410.6 | 411.5 | 0.9 |  |
|  | AH | 46,540 | 116 | 1,115 | 7.40 | 412.6 | 412.6 | 413.3 | 0.7 |  |
|  | AI | 47,210 | 200 | 1,607 | 5.10 | 413.6 | 413.6 | 414.6 | 1.0 |  |
|  | ¹Feet above confluence with Contoocook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | WARNER RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Warner River (continued) |  |  |  |  |  |  |  |  |  |
|  | AJ | 47,580 | 86 | 1,196 | 6.90 | 415.0 | 415.0 | 415.3 | 0.3 |  |
|  | AK | 47,890 | 125 | 1,440 | 5.70 | 415.3 | 415.3 | 416.1 | 0.8 |  |
|  | AL | 49,100 | 147 | 1,736 | 4.70 | 416.8 | 416.8 | 417.6 | 0.8 |  |
|  | AM | 49,419 | 200 | 2,370 | 3.50 | 417.7 | 417.7 | 418.3 | 0.6 |  |
|  | AN | 51,240 | 186 | 1,848 | 4.50 | 418.5 | 418.5 | 419.2 | 0.7 |  |
|  | AO | 53,290 | 400 | 4,308 | 1.90 | 420.7 | 420.7 | 421.3 | 0.6 |  |
|  | AP | 54,560 | 560 | 4,924 | 1.70 | 421.0 | 421.0 | 421.8 | 0.8 |  |
|  | AQ | 55,140 | 300 | 2,302 | 3.60 | 421.0 | 421.0 | 421.9 | 0.9 |  |
|  | AR | 55,400 | 170 | 1,344 | 4.60 | 421.2 | 421.2 | 422.2 | 1.0 |  |
|  | AS | 55,558 | 126 | 1,130 | 5.50 | 421.5 | 421.5 | 422.4 | 0.9 |  |
|  | AT | 57,430 | 135 | 1,391 | 4.50 | 423.2 | 423.2 | 423.9 | 0.7 |  |
|  | AU | 59,390 | 125 | 1,145 | 5.50 | 424.9 | 424.9 | 425.6 | 0.7 |  |
|  | AV | 61,220 | 122 | 602 | 10.40 | 443.1 | 443.1 | 443.1 | 0.0 |  |
|  | AW | 61,282 | 155 | 1,292 | 4.80 | 446.2 | 446.2 | 447.0 | 0.8 |  |
|  | AX | 61,399 | 92 | 885 | 7.00 | 446.6 | 446.6 | 447.3 | 0.7 |  |
|  | AY | 63,080 | 300 | 1,859 | 3.40 | 448.7 | 448.7 | 449.1 | 0.4 |  |
|  | AZ | 64,305 | 461 | 2,598 | 2.40 | 449.8 | 449.8 | 450.4 | 0.6 |  |
|  | BA | 66,730 | 297 | 1,266 | 4.90 | 452.6 | 452.6 | 452.8 | 0.2 |  |
|  | BB | 68,570 | 138 | 668 | 9.30 | 461.3 | 461.3 | 461.3 | 0.0 |  |
|  | BC | 69,470 | 136 | 757 | 8.20 | 468.5 | 468.5 | 468.9 | 0.4 |  |
|  | BD | 71,780 | 100 | 935 | 6.70 | 507.0 | 507.0 | 507.1 | 0.1 |  |
|  | BE | 72,150 | 200 | 1,523 | 4.10 | 508.2 | 508.2 | 508.3 | 0.1 |  |
|  | BF | 74,140 | 173 | 1,242 | 3.60 | 509.3 | 509.3 | 509.8 | 0.5 |  |
|  | BG | 74,420 | 200 | 903 | 4.90 | 509.4 | 509.4 | 509.8 | 0.4 |  |
|  | BH | 74,880 | 250 | 1,357 | 3.30 | 510.3 | 510.3 | 511.1 | 0.8 |  |
|  | BI | 75,090 | 132 | 1,162 | 3.80 | 510.8 | 510.8 | 511.8 | 1.0 |  |
|  | ¹Feet above confluence with Contoocook River |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | WARNER RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Warner River (continued) |  |  |  |  |  |  |  |  |  |
|  | BJ | 75,340 | 80 | 919 | 4.90 | 511.6 | 511.6 | 512.6 | 1.0 |  |
|  | BK | 75,690 | 70 | 924 | 4.80 | 511.9 | 511.9 | 512.8 | 0.9 |  |
|  | BL | 77,044 | 80 | 702 | 6.40 | 519.4 | 519.4 | 520.3 | 0.9 |  |
|  | BM | 77,155 | 150 | 1,358 | 3.30 | 520.1 | 520.1 | 521.0 | 0.9 |  |
|  | BN | 77,490 | 146 | 1,628 | 2.70 | 520.5 | 520.5 | 521.3 | 0.8 |  |
|  | BO | 78,810 | 200 | 1,558 | 2.90 | 520.9 | 520.9 | 521.6 | 0.7 |  |
|  | BP | 80,520 | 45 | 301 | 14.80 | 544.9 | 544.9 | 544.9 | 0.0 |  |
|  | BQ | 81,640 | 83 | 757 | 5.90 | 558.0 | 558.0 | 558.1 | 0.1 |  |
|  | BR | 81,897 | 48 | 387 | 11.50 | 562.4 | 562.4 | 562.4 | 0.0 |  |
|  | BS | 83,260 | 57 | 446 | 10.00 | 589.1 | 589.1 | 589.9 | 0.8 |  |
|  | BT | 85,060 | 61 | 504 | 8.80 | 612.4 | 612.4 | 612.8 | 0.4 |  |
|  | BU | 85,890 | 50 | 439 | 10.20 | 624.8 | 624.8 | 625.8 | 1.0 |  |
|  | BV | 87,020 | 55 | 322 | 13.90 | 628.3 | 628.3 | 628.3 | 0.0 |  |
|  | BW | 87,190 | 71 | 884 | 5.00 | 638.3 | 638.3 | 638.3 | 0.0 |  |
|  | BX | 89,750 | 492 | 1,750 | 2.00 | 641.9 | 641.9 | * | * |  |
|  | BY | 89,823 | 485 | 2,600 | 1.40 | 642.2 | 642.2 | * | * |  |
|  | BZ | 91,780 | 221 | 1,790 | 2.00 | 642.6 | 642.6 | * | * |  |
|  | CA | 94,078 | 352 | 2,010 | 1.80 | 643.1 | 643.1 | * | * |  |
|  | CB | 94,160 | 297 | 2,050 | 1.70 | 643.3 | 643.3 | * | * |  |
|  | CC | 100,353 | 699 | 4,240 | 0.70 | 643.9 | 643.9 | * | * |  |
|  | CD | 100,552 | 86 | 723 | 4.30 | 643.9 | 643.9 | * | * |  |
|  | ¹Feet above confluence with Contoocook River *Data not available |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | WARNER RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE | WIDTH (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | West Channel Suncook River |  |  |  |  |  |  |  |  |  |
|  | A | 0.3001 | 200 | 1,764 | 2.08 | 312.1 | 312.1 | 312.9 | 0.8 |  |
|  | B | 0.4301 | 107 | 825 | 4.45 | 312.2 | 312.2 | 313.2 | 1.0 |  |
|  | C | 0.6101 | 70 | 362 | 10.15 | 316.3 | 316.3 | 316.4 | 0.1 |  |
|  | D | 0.8401 | 97 | 931 | 3.95 | 320.7 | 320.7 | 321.2 | 0.5 |  |
|  | E | 0.9701 | 90 | 620 | 5.93 | 321.6 | 321.6 | 322.1 | 0.5 |  |
|  | Williams Brook |  |  |  |  |  |  |  |  |  |
|  | A | 0.0272 | 92 | 562 | 2.60 | 412.2 | 411.15 | 421.1 | 1.0 |  |
|  | B | 0.1882 | 62 | 404 | 3.70 | 413.7 | 413.7 | 414.2 | 0.5 |  |
|  | C | 0.5602 | 118 | 656 | 2.00 | 415.6 | 415.6 | 416.6 | 1.0 |  |
|  | D | 0.8072 | 48 | 274 | 4.70 | 417.3 | 417.3 | 418.1 | 0.8 |  |
|  | E | 1.1872 | 80 | 253 | 5.10 | 428.0 | 428.0 | 428.6 | 0.6 |  |
|  | F | 1.3082 | 26 | 279 | 4.60 | 441.4 | 441.4 | 441.4 | 0.0 |  |
|  | Winnipesaukee River |  |  |  |  |  |  |  |  |  |
|  | A | 115.9543 | 180 | 2,194 | 2.60 | 271.7 | 271.7 | 272.7 | 1.0 |  |
|  | B | 116.1853 | 157 | 2,140 | 2.70 | 286.0 | 286.0 | 286.0 | 0.0 |  |
|  | C | 116.5753 | 130 | 1,274 | 4.00 | 287.5 | 287.5 | 287.7 | 0.2 |  |
|  | D | 116.9283 | 185 | 1,526 | 3.30 | 300.4 | 300.4 | 300.4 | 0.0 |  |
|  | E | 117.0803 | 135 | 2,097 | 2.40 | 322.7 | 322.7 | 322.7 | 0.0 |  |
|  | F | 117.5323 | 126 | 615 | 9.30 | 353.2 | 353.2 | 353.3 | 0.1 |  |
|  | G | 117.9373 | 100 | 618 | 9.30 | 385.0 | 385.0 | 385.4 | 0.4 |  |
|  | H | 118.3413 | 159 | 1,349 | 4.20 | 406.1 | 406.1 | 406.3 | 0.2 |  |
|  | I | 119.0853 | 181/ 984 | 1,475 | 3.90 | 407.6 | 407.6 | 407.9 | 0.3 |  |
|  | J | 119.7943 | 145/ 704 | 1,029 | 5.60 | 410.3 | 410.3 | 410.4 | 0.1 |  |
|  | K | 120.6763 | 106/ 534 | 731 | 7.80 | 415.8 | 415.8 | 416.1 | 0.3 |  |
|  | ¹Miles above confluence with Suncook River 4Width/ width within county boundary 2Miles above confluence with Winnipesaukee River 4Miles above confluence with Winnipesaukee River 3Miles above Newburyport Light, Newburyport, MA |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | WEST CHANNEL SUNCOOK RIVER – WILLIAMS BROOK – WINNIPESAUKEE RIVER |

|  | FLOODING SOURCE | FLOODWAY | BASE FLOOD WATER-SURFACE ELEVATION (FEET NAVD) |  |
| --- | --- | --- | --- | --- |
|  | CROSS SECTION | DISTANCE1 | WIDTH2 (FEET) | SECTION AREA (SQUARE FEET) | MEAN VELOCITY (FEET PER SECOND) | REGULATORY | WITHOUT FLOODWAY | WITH FLOODWAY | INCREASE |  |
|  | Winnipesaukee River |  |  |  |  |  |  |  |  |  |
|  | (continued) |  |  |  |  |  |  |  |  |  |
|  | L | 121.094 | 99/ 49 | 686 | 8.30 | 446.1 | 446.1 | 446.1 | 0.0 |  |
|  | M | 121.275 | 140/ 68 | 1,386 | 4.10 | 451.6 | 451.6 | 452.5 | 0.9 |  |
|  | N | 121.610 | 180/ 97 | 1,260 | 4.50 | 454.2 | 454.2 | 454.5 | 0.3 |  |
|  | O | 121.985 | 175/ 87 | 1,004 | 5.70 | 456.2 | 456.2 | 456.3 | 0.1 |  |
|  | P | 122.583 | 136/ 66 | 591 | 9.70 | 462.5 | 462.5 | 463.0 | 0.5 |  |
|  | Q | 122.915 | 169/ 81 | 1,148 | 5.00 | 468.1 | 468.1 | 468.2 | 0.1 |  |
|  | R | 124.027 | 275/ 137 | 2,463 | 2.20 | 470.1 | 470.1 | 470.3 | 0.2 |  |
|  | ¹Miles above Newburyport Light, Newburyport, MA 2Width/ width within county boundary |  |
| TABLE 6 | FEDERAL EMERGENCY MANAGEMENT AGENCY MERRIMACK County, NH (ALL JURISDICTIONS) | FLOODWAY DATA |
|  |  | WINNIPESAUKEE RIVER |